## Slide 1: Position Interlink for Extended Interface Emulation
Encoder Multiplexing System
Multi-Axis Animatronic Figure System · Entertainment Systems
RP2350 · PIO · Hamming ECC · Full-Duplex · Source-Synchronous

## Slide 2: What Is an Animatronic Encoder System?
Encoders: The Eyes of Every Joint
Every motor in an animatronic figure has an encoder — a sensor that reports exactly where the joint is
Encoders output two square wave signals (A and B) that shift in phase as the motor turns
By counting the pulses and comparing A vs. B, the servo drive knows position and direction
The Wiring Problem
Each encoder needs dedicated wires running from the motor to the servo drive
With 17 motors across the arms and neck, that's 68 wires routed through narrow joint cavities that flex continuously
Wire damage is the #1 failure mode — flex fatigue breaks wires, causing encoder loss and figure downtime
The Idea
Capture all encoder signals locally, send them over a single high-speed serial link, and regenerate identical outputs so the drives never know the difference
Fewer wires through joints = less flex fatigue = dramatically reduced failure rate

## Slide 3: The Challenge
Primary Failure Mode: Wire Damage
On complex animatronic figures, the #1 cause of animatronic downtime is wire damage and failure
68 encoder wires routed through narrow joint cavities that flex continuously during show operation
More wires = more flex fatigue, more potential break locations, harder troubleshooting
Wire routing exercises underway to improve cable paths — but path optimization alone cannot solve the volume problem
The Fix: Fewer Wires + Modular Design
Multiplex encoder signals to drastically reduce wire count through joints
Enable quick-disconnect modular arm assemblies for scheduled PM cycles
Regenerate identical outputs so drives require zero programming changes

## Slide 4: Wire Count: Before vs. After
BEFORE — Traditional Per-Motor Wiring
Node / Signal
Motors
Wires
Left Arm (A, B, Pwr, 0V each)
5
20
Right Arm (A, B, Pwr, 0V each)
5
20
Neck + Arm Out/Fwd (A, B, Pwr, 0V)
7
28
TOTAL (17 encoders)
17
68 wires
AFTER — Custom Bridge Protocol (3 Nodes)
Function
Per Node
x3 Nodes
Upstream Data (3 diff pairs)
6 wires
18
Downstream Response (1 diff pair)
2 wires
6
Board Power + 0V
2 wires
6
Encoder Power + 0V
2 wires
6
TOTAL (3 nodes)
12/node
36 wires
Node Allocation
Left Arm Node
5 motors
Hand, wrist, elbow, etc.
Right Arm Node
5 motors
Hand, wrist, elbow, etc.
Neck Node
7 motors
3 neck + L/R arm out + L/R arm fwd
47% Wire Reduction 68 wires (17 encoders) → 36 wires (3 bridge nodes)

## Slide 5
Transparent Emulation
The Core Principle: Zero Change at the Drive
Remote board regenerates A/B quadrature signals electrically identical to original encoder outputs
Servo drives require zero firmware or configuration changes
From the drive's perspective, the encoder is still directly wired — it simply cannot tell
How It Works
Capture: PIO state machines decode A/B quadrature at the encoder board
Transport: Position deltas serialized over the high-speed link with error correction
Regenerate: Remote board reconstructs matching A/B pulse trains output to the drives
Enables Modular Arm Swap
Transparent emulation + single-cable node = simple Lemo quick-disconnect interface
Swap an entire arm assembly in minutes instead of troubleshooting individual wires for hours
Signal Flow
Encoders (A/B signals)
Encoder Board (PIO Capture)
3↑ / 1↓ pairs
Remote Board (Regenerate)
Servo Drives (sees no change)
✓ Identical A/B output

## Slide 6: System Architecture
Left Arm
5 motors
A/B encoders
Left Arm Node
RP2350 (Pico 2)
PIO TX + Hamming ECC
Remote Board
RP2350 (Pico 2)
PIO RX + Hamming Decode
Servo Drives
Regenerated A/B
RS-422 Output
Right Arm
5 motors
A/B encoders
Right Arm Node
RP2350 (Pico 2)
PIO TX + Hamming ECC
Remote Board
RP2350 (Pico 2)
PIO RX + Hamming Decode
Servo Drives
Regenerated A/B
RS-422 Output
Neck
7 motors
3 neck + 2L arm + 2R arm
Neck Node
RP2350 (Pico 2)
PIO TX + Hamming ECC
Remote Board
RP2350 (Pico 2)
PIO RX + Hamming Decode
Servo Drives
Regenerated A/B
RS-422 Output
4 diff pairs each
3↑ up / 1↓ down

## Slide 7
Modular Maintenance Strategy
Quick-Disconnect Modular Arms
Each arm assembly connects via Lemo quick-disconnect connectors
Only two connections per arm: motor power harness + one encoder node cable
Multiplexing makes this possible — without the node, each motor needs its own encoder cable individually
Scheduled PM Cycle
A second complete set of arms pre-built and maintained as ready spares
On scheduled PM: disconnect two Lemo connectors, swap in fresh arm, reconnect
Removed arm goes back to shop for full rebuild and inspection
Continuous rotation: field arm always fresh, shop arm always being rebuilt
Why This Changes Everything
Downtime: hours of in-situ troubleshooting → minutes of connector swap
Proactive scheduled maintenance replaces reactive failure response
Wire damage repairs happen on the bench, not inside a dark figure cavity at 2 AM
Lemo Disconnect
SWAP
Minutes, not hours

## Slide 8: Physical Layer
Cable Bundle per Node (12 Conductors)
Pair 1-3 Upstream — encoder data to remote board (differential)
Pair 4 Downstream — response/status back to encoder board
Power Board power + 0V, encoder power + 0V
Encoder Signals (per motor)
A and B quadrature channels only — no Z index pulse
Arm nodes: 5 encoders each | Neck node: 7 encoders
Signal Integrity
Differential signaling on all data pairs for noise immunity
120Ω termination at both ends of each pair

## Slide 9: Source-Synchronous Protocol
What Is Source-Synchronous?
The transmitter sends a clock signal alongside the data — the receiver samples data on each clock edge
No baud rate negotiation needed — both sides are locked to the same clock
Eliminates clock drift and makes timing deterministic at high speeds
Our 3 Upstream Pairs
CLK pair: PIO-generated clock via sideset at 5 Mbit/s, sent alongside data
DATA pair: Serialized frame data, sampled on the rising CLK edge by the receiver
IDLE pair: Signals when data is valid vs. inter-frame gap — prevents false sync
Downstream (1 Pair)
Return channel for acknowledgment, status, and health monitoring
CLK
DATA
IDLE
← Data Valid →
Gap
5 Mbit/s

## Slide 10: Frame Format
Sync0
0xA5
Sync1
0x5A
Seq
uint8
Flags
uint8
1B
1B
1B
1B
Delta 0
int32
4B
Delta 1
int32
4B
Delta 2
int32
4B
Delta 3
int32
4B
Delta 4
int32
4B
Delta 5
int32
4B
Delta 6
int32
4B
Delta 7
int32
4B
HSEC
ECC
CRC16
CCITT
4B
2B
Header 4 B
Payload 32 B (8 axes × int32)
Check 6 B
Total Frame: 42 bytes (336 bits) — striped across 3 pairs = 112 bits/pair
Production Bandwidth Budget (25 µs / 40 kHz)
Per-pair baud: 10 Mbps (conservative RS-422)
Wire capacity: 3 pairs × 250 bits = 750 bits/frame
Frame uses: 336 bits (112 bits/pair) → 11.2 µs wire time
Utilization: 44.8% — ~2.2× headroom at 8 axes
Processing budget: 13.8 µs remaining for encode/decode
int32 range: ±2.1 billion counts/frame — unlimited resolution
Maximum Axis Capacity per Node
750 bits available − 48 bits overhead = 702 bits
With ~12.5% Hamming overhead → 614 payload bits
614 bits ÷ 32 bits/axis = up to 19 axes per node at int32
Standard 8-axis: fits with room for diagnostics or more axes
Example config: arms (5), neck (7) — all fit in one frame at full resolution
Scales to larger figures without protocol changes

## Slide 11: Hamming Error Correction
Why Hamming for This Link?
Real-time motion data cannot tolerate retransmission latency
Hamming corrects single-bit errors in-place — no round-trip needed
CRC16 remains as a secondary check for multi-bit burst errors
Error Handling Strategy
1-bit error: Hamming corrects automatically, frame accepted
2-bit error: Hamming detects but cannot correct; CRC confirms, frame dropped
Burst error: CRC catches, frame rejected; timeout logic engages if sustained

## Slide 12: PIO Engine Deep Dive
POC Platform: RP2350 (Pi Pico 2)
Pi Pico 2 is used strictly for prototyping and proof-of-concept
Production system will migrate to FPGA once the protocol is validated
Pico 2 allows rapid iteration on protocol and firmware before committing to FPGA design
Why PIO Works for POC
Programmable I/O state machines run independently of CPU cores
Deterministic cycle-accurate bit timing — zero jitter from interrupts or scheduling
RP2350: 3 PIO blocks x 4 state machines = 12 SMs
DMA channels feed PIO FIFOs — CPU free for Hamming/CRC computation
Written in C using Pico SDK — PIO logic translates directly to FPGA HDL later

## Slide 13: Upstream Protocol (3 Pairs)
3 Upstream Pairs: Encoder Board → Remote Board
Each pair carries serialized frame data via PIO-driven custom protocol
Frame data striped across 3 pairs for increased throughput
Variable axis count per node: 5 (arms) or 7 (neck) A/B encoders
Data Flow per Frame
Step 1: RS-422 receivers sample A/B encoder inputs from all motors on node
Step 2: RP2350 computes deltas, encodes Hamming ECC + CRC16
Step 3: DMA pushes frame bytes into 3 PIO TX FIFOs for parallel transmission
Step 4: Remote board reassembles frame from 3 PIO RX state machines

## Slide 14: Encoder Board — TX Frame Sequence
1
Sample Encoders
PIO state machines continuously decode A/B quadrature from all motor encoders on this node. Counts update in real-time — no CPU involvement.
2
Snapshot & Compute Deltas
At each 25 µs frame tick, CPU atomically reads all PIO counters. Computes signed int32 delta per axis since last snapshot.
3
Build Frame
Pack header (sync, seq, flags) + 8 axis deltas into a 42-byte frame buffer. Increment sequence counter.
4
Encode ECC + CRC
Compute Hamming SECDED parity over payload bytes. Append Hamming ECC (4B) and CRC16-CCITT (2B) to frame.
5
Stripe & Serialize
DMA splits frame into 3 equal stripes (14 bytes each). Each stripe is pushed into a separate PIO TX FIFO.
6
Transmit
3 PIO state machines clock out data + source clock simultaneously over 3 RS-422 differential pairs. Wire time: 11.2 µs.
Full cycle repeats every 25 µs — Steps 1–4 run on CPU cores — Steps 5–6 run on PIO + DMA (zero CPU)

## Slide 15: Remote Board — RX Frame Sequence
1
Receive & Sync
3 PIO RX state machines sample incoming data on each source-clock edge. Preamble detector locks to sync bytes (0xA5, 0x5A) on each pair.
2
Reassemble Frame
DMA collects stripe data from 3 PIO RX FIFOs. Interleaved bytes are de-striped back into the original 42-byte frame buffer.
3
Verify CRC16
CRC16-CCITT computed over received data bytes and compared to the frame's CRC field. Mismatch → frame rejected, error counter incremented.
4
Hamming ECC Correct
SECDED Hamming check on payload. Single-bit errors corrected in-place automatically. Double-bit errors detected → frame dropped with CRC confirmation.
5
Apply Deltas
Validated int32 deltas added to each axis position accumulator. Sequence number checked for gaps — missed frames logged to diagnostics.
6
Regenerate A/B Pulses
PIO state machines step the A/B quadrature outputs by the delta count for each axis. Drives see electrically identical encoder signals — zero change required.
Steps 1–2 run on PIO + DMA (zero CPU) — Steps 3–5 run on CPU cores — Step 6 runs on PIO output state machines

## Slide 16: Downstream Protocol (1 Pair)
1 Downstream Pair: Remote Board → Encoder Board
Low-bandwidth return channel for acknowledgment and status
Single differential pair is sufficient — response data is much smaller than encoder data
Downstream Payload
Frame ACK Sequence acknowledgment for flow control
Status flags Remote board health, drive acceptance status, error counters
Configuration Runtime parameter updates (future expansion)
Heartbeat Confirms remote board is alive — feeds encoder board watchdog

## Slide 17: Timing & Performance Budget
Key Timing Parameters
POC frame period: 50 µs (20 kHz) — current bench target on Pi Pico 2
Production target: 25 µs (40 kHz) — FPGA enables tighter frame period
Target baud: 10 Mbps per pair (RS-422 differential)
Standard frame: 42 bytes (336 bits) — 8 axes × int32 per node
Comm timeout: 250 µs (10 missed frames triggers fault)
Production Bandwidth Budget
3 pairs × 10 Mbps = 30 Mbps aggregate — 336 bits/frame uses 44.8%
Wire time: 11.2 µs — leaves 13.8 µs for encode, decode, and processing
Max capacity: up to 19 axes per node at int32 within 25 µs budget

## Slide 18: Speed vs. Reliability
40 kHz Is Already Generous
Animatronic show motions are choreographed and slow relative to servo loop rates
25 µs frame period is far faster than the mechanical time constants of these joints
A single dropped frame is absorbed by the next update 25 µs later — the speed problem is already solved
The Real Metric: Reliability
POC bench shows 92% packet success on GPIO jumper wires without ECC — getting to 99.99%+ matters more than pushing speed
Hamming ECC + CRC16 + RS-422 differential on a real PCB will close this gap
~4× bandwidth headroom means ECC overhead fits without sacrificing frame rate
What FPGA Buys (It's Not Speed)
Determinism Pure parallel logic — no OS, no interrupt latency, no firmware edge cases
True parallelism All encoder channels decoded simultaneously in dedicated fabric
Production reliability No stack overflows, no memory leaks — hardware can't crash like firmware

## Slide 19: Fault Handling & Recovery
Fault Detection
Comms timeout No valid frame for >500 µs → stop pulse regeneration, assert fault pin
CRC burst Keep last valid state, continue timeout monitoring
Seq gap Missed frame counter increments; logged for diagnostics
Recovery
Require 4 consecutive valid frames before clearing fault state
Prevents flapping during intermittent cable issues
Hamming corrections logged but do not trigger fault — they are transparent repairs
All error counters exposed via downstream response for monitoring

## Slide 20: Current Results
Bench Test Results (GPIO Jumper Wires, Arduino C Firmware)
Link speed: 5 Mbit/s source-synchronous serial
Packet success: 92% (before Hamming ECC — expected to improve significantly)
Latency: <2 ms end-to-end
Encoder decode: 4-channel PIO quadrature decode verified, counts propagating master to slave
Completed Milestones
RP2040 PIO quadrature encoder decode x4
5 Mbit/s source-synchronous PIO serial link
CRC-16 packet framing with preamble sync
Live OLED display on both master and slave nodes

## Slide 21: Bring-Up & Validation Plan
A
Pre-Power
Visual inspection
Continuity checks
Polarity verification
B
Power-Up
5V/3.3V within tolerance
No abnormal current
Stable under load
C
Comms Link
Termination enabled
UART link up
CRC errors = zero
D
Single Axis
Encoder A/B at Tx outputs
Delta tracks movement
Drive accepts signals
E
Multi-Axis
Add axes one at a time
No crosstalk/swapping
High-rate stress test
F
Fault Test
Unplug cable test
Timeout within spec
Clean recovery verified
Record for validation: Max pulse rate | End-to-end latency | Jitter summary | Error counters (CRC, seq gaps, timeouts)

## Slide 22: Next Steps & Roadmap
Phase 1: POC (Current — Pi Pico 2)
Validate protocol, PIO encode/decode, Hamming ECC, and signal regeneration
Confirm servo drives accept regenerated outputs with zero configuration changes
Phase 2: Bench Validation + Wire Routing
3-node stress test: left arm (5), right arm (5), neck (7) — 17 encoders
Continue wire routing exercises to optimize remaining cable paths
Phase 3: FPGA Migration — Reliability, Not Speed
Same protocol and frame format — FPGA buys determinism, not higher baud rate
Pure parallel logic — no firmware edge cases, no stack overflows, no memory leaks
Custom PCB with FPGA, RS-422 transceivers, Lemo quick-disconnect interface
Phase 4: Modular Arm PM Cycle
Second set of arms pre-built and ready as hot-swap spares
Lemo quick-disconnect for motor power + single node connector per arm
Swap arm in field, send removed arm to shop for rebuild — scheduled PM cycle